/*******************************************************

RGB Color Controller

-tests buttons and slider interface with touchscreen

Pic18F4580

8Mhz Internal Clock

320x240 TFT LCD, HX8347

Touchscreen controller ADS7843

5/12/11

Ryan Milewski

blackrynius.wordpress.com

********************************************************/

#include <p18f4580.h>

#include <delays.h>

#include <lcd320x240.h>

#include <stdio.h>

#include <ads7843.h>

#include <lcd320x240.c>

#include <ads7843.c>

#pragma config OSC = IRCIO67

#pragma config WDT = OFF

#pragma config LVP = OFF

#pragma config DEBUG=OFF

#pragma config PBADEN = OFF

#pragma	config MCLRE = ON

#pragma config BOREN = OFF

#pragma config STVREN = OFF

unsigned int new_color = 0;

unsigned int old_color = 1;

char temp_str[];

unsigned int TP_X,TP_Y;

int lx,ly,i;

float level;

int level_1=0;

int level_2=0;

int level_3=0;

int level_1_old = 0;

int level_2_old = 0;

int level_3_old = 0;

unsigned int red_value = 0;

unsigned int green_value = 0;

unsigned int blue_value = 0;

void main(void)

{

//port setup----------------------------------------

//Initialize ports per datasheet

PORTA = 0;

PORTC = 0;

PORTD = 0;

PORTE = 0;

ADCON0bits.ADON = 0;	// Analog OFF

ADCON1 = 0x0f;			//All analog ports digital

CMCON = 0x07;			//All comparators off

TRISA = 0b11000000;

TRISC = 0;

TRISD = 0;

TRISE = 0;

//==================================================

PORTAbits.RA1 = 1;

LCD_init();

LCD_fill_screen(BLACK);

new_color = RED;

//LCD_draw_rect(0,0,239,10,WHITE,1);

LCD_put_rom_str("RGB Color Control",10,1,BLUE,BLACK);

LCD_draw_line(0,12,239,12,RED);

spistart();

//LCD_put_rom_str("X:",5,115,RED,BLACK);

//LCD_put_rom_str("Y:",130,115,RED,BLACK);

//Draw screen-----------------------------------------------

//Graph boarders

LCD_draw_rect(19,49,51,201,WHITE,0);

LCD_draw_rect(79,49,111,201,WHITE,0);

LCD_draw_rect(139,49,171,201,WHITE,0);

//MAX buttons

LCD_draw_rect(20,20,50,40,WHITE,1);

LCD_put_rom_str("MAX",21,21,BLACK,WHITE);

LCD_draw_rect(80,20,110,40,WHITE,1);

LCD_put_rom_str("MAX",81,21,BLACK,WHITE);

LCD_draw_rect(140,20,170,40,WHITE,1);

LCD_put_rom_str("MAX",141,21,BLACK,WHITE);

//MIN buttons

LCD_draw_rect(20,220,50,240,WHITE,1);

LCD_put_rom_str("MIN",21,221,BLACK,WHITE);

LCD_draw_rect(80,220,110,240,WHITE,1);

LCD_put_rom_str("MIN",81,221,BLACK,WHITE);

LCD_draw_rect(140,220,170,240,WHITE,1);

LCD_put_rom_str("MIN",141,221,BLACK,WHITE);

LCD_put_rom_str("Color: ",10,250,PURPLE,BLACK);

//-----------------------------------------------------------

while(1)

{

PORTAbits.RA0 = 1;

PORTAbits.RA1 = 0;

if(D_IRQ==0)

{

ADS7843_getxy();

lx= (TP_X/17);

ly= 350 - (TP_Y/11);

if(ly>=20 && ly<=50)//MAX button area-----

{

level = 100;

if(lx>=20 && lx<=50)

{

level_1 = level;

}

else if(lx>=80 && lx<=110)

{

level_2 = level;

}

else if(lx>=140 && lx<=170)

{

level_3 = level;

}

}//end of max button area-----------------

if(ly>=50 && ly<=200)//Graph area---------

{

level = (100-((ly-50)*.667));

if(lx>=20 && lx<=50)

{

level_1 = level;

}

else if(lx>=80 && lx<=110)

{

level_2 = level;

}

else if(lx>=140 && lx<=170)

{

level_3 = level;

}

}//end of bar graph touch area------------

if(ly>=220 && ly<=240)//MIN button area---

{

level = 0;

if(lx>=20 && lx<=50)

{

level_1 = level;

}

else if(lx>=80 && lx<=110)

{

level_2 = level;

}

else if(lx>=140 && lx<=170)

{

level_3 = level;

}

}//end of min button touch area------------

}//end of touchscreen--------------------------

if(level_1 != level_1_old)

{

LCD_bar_graph(20,50,50,200,RED,BLACK,level_1);

level_1_old = level_1;

red_value = 31*level_1*.01;

}

else if(level_2 != level_2_old)

{

LCD_bar_graph(80,50,110,200,GREEN,BLACK,level_2);

level_2_old = level_2;

green_value = 63*level_2*.01;

}

else if(level_3 != level_3_old)

{

LCD_bar_graph(140,50,170,200,BLUE,BLACK,level_3);

level_3_old = level_3;

blue_value = 31*level_3*.01;

}

new_color = (red_value<<11)+(green_value<<5)+blue_value;

if(new_color != old_color)

{

sprintf(temp_str, "0x%02x  0x%02x  0x%02x",red_value,green_value,blue_value);

LCD_put_str(temp_str, 10, 270, CYAN, BLACK);

sprintf(temp_str,"0x%04x", new_color);

LCD_put_str(temp_str, 100, 300, WHITE, BLACK);

LCD_draw_rect(170,250,230,310,new_color,1);

old_color = new_color;

}

PORTAbits.RA1 = 0;

}//end of main while

}//end of main()